## Slide 1: SimpliVity Technical Deep Dive
Zhang Gang
Channel Solution Architect, Asia

## Slide 2: Key Elements
SimpliVity Federation
VMware Datacenter (Cluster)
VMware Datacenter (Cluster)
+
vCenter Server
Supports vCenter linked mode
vSphere Web Client
SimpliVity Web Plug-in
SimpliVity Arbiter
Notes: First, you should know that SimpliVity OmniStack systems are essentially ESXi servers, with storage, that are added to vCenter datacenters and clusters. Multiple OmniStack systems form a SimpliVity Federation that can span multiple datacenters and even multiple vCenters operating in linked mode. We’ll talk more about this later but OmniStack systems and their software releases are built on specific versions of ESXi and as such are intended for specific versions of vCenter Server and the vSphere Client.
Since all management is done directly through vSphere, SimpliVity provides a Plug-in which adds the SimpliVity functionality through a new SimpliVity tab and by right-clicks in the Inventory View. Each OmniStack ships with a SimpliVity OVF image used for deployment so the vSphere Client must have VMware OVF Tools installed.
On the vCenter Server a SimpliVity Arbiter is installed which provides a communication mechanism unique to OmniStack systems.

## Slide 3: What is a Federation?
From as small as 1 or 2+0
To 4+4
And well beyond…
VMware Datacenter (Cluster)
+
0
VMware Datacenter (Cluster)
VMware Datacenter (Cluster)
+
VMware Datacenter (Cluster)
+
VMware Datacenter
VMware Datacenter
VMware Datacenter
VMware Datacenter
VMware Datacenter
VMware Datacenter
+
+
+
+
+
VMware Datacenter
, or 2+1
+
VMware Datacenter (Cluster)
VMware Datacenter (Cluster)

## Slide 4: Data IO Path

## Slide 5: OmniStack Architecture
ESXi Kernel
OmniStack Virtual Controller (OVC)
57-100 GB vRAM
Read Cache
OmniStack Accelerator
Write Ack
Inline Dedup and Compression
Sequentialization
RAID Controller
SSD
SSD
SSD
SSD
RAID 6 or 60 on HDD
RAID 1 or 5 on SSD

## Slide 6: OmniStack Architecture Write I/O
ESXi Kernel
OVC
OA
RAID
SSD
SSD
SSD
SSD
HDD
ESXi Kernel
OVC
OA
RAID
SSD
SSD
SSD
SSD
HDD
1. VM Writes a Block
4. I/O is acknowledged and persisted on OA
5. I/O is acknowledged to VM
6. I/O is deduplicated, If not unique complete.
6
6
7. If I/O is unique, I/O is compressed and serialized.
7
7
8. I/O is destaged to HDD pool on each node.
Primary OmniStack
Secondary OmniStack
2. ESXi Sends Block via NFS
Storage
3. OVC Sends Block to local and remote OA
Federation
VM

## Slide 7: OmniStack Architecture Read I/O
ESXi Kernel
OVC
OA
RAID
SSD
SSD
SSD
SSD
HDD
ESXi Kernel
OVC
OA
RAID
SSD
SSD
SSD
SSD
HDD
VM
1. VM Requests a Block
2. ESXi Sends Read Request via NFS
3. OVC knows location of block and reads from fastest performing location:
A. OVC Cache
B. SSD
C. HDD Pool
A
B
C
4. OVC Sends Block to VM
5. OVC Determines if I/O should be placed in SSD Pool
Primary OmniStack
Secondary OmniStack

## Slide 8: Data Virtualization Platform

## Slide 9: Data Virtualization Platform
Data Virtualization Platform
Data Management Layer
File System
x86 platform
x86 platform
x86 platform
VM2
VM4
Hypervisor
Hypervisor
Hypervisor
Presentation Layer
VM1
Datastore 1
VM2
Object Store
VM1
VM3
VM4
VM5
VM5
Datastore 2
VM4
VM3
VM2
VM1
VM3
VM1
VM3
VM5
Notes: Within the Data Virtualization Platform there are a few layers with different roles.
At the top is the presentation layer which makes VMs available to the hypervisor. VMs are a pointer down to Data Containers in the File System within the Data Management Layer. Not all of the data containers in the File System are VMs, some are backups of VMs.
The data containers in the File System point to trees of unique objects in the object store, which are deduplicated.
You can think of the Presentation and file system as very thin layers on top of the large deduplicated object store.
If we use SimpliVity to clone a VM
<click>
Only the data container is copied and the presentation layer is updated to have a new VM pointing to the new Data Container. None of the actual data blocks of the source VM were copied, since we already have the unique blocks. This SimpliVity clone operation completes, and the VM appears in the vCenter inventory, in a few seconds, with virtually no I/O.
The process to backup a VM is quite similar
<click>
We make a copy of the Data Container but since it’s a backup we don’t need to update the presentation layer. Again there is almost no IO because we have already stored all the unique blocks. Only the file system needs to be updated.
A backup is important, but only because we need to do restores. When we restore from the backup it is the same operation as a SimpliVity clone.
<click>
We make a copy of the Data Container that is the backup and update the presentation layer to show the restored VM to vSphere. Again there is no need to copy large amounts of data as we already have the unique blocks stored.
You can see that cloning, backup, and restore are basically about copying the Data Container and possibly updating the presentation layer, if the result is a VM.
Because there is virtually no I/O, no load on the disks, there is no impact to any VMs performance. No noisy neighbor problems when performing backup and restore functions. We can backup or clone VMs any time, even several times per hour, without impacting performance.
All of the disk and SSD performance is available to the running VMs, rather than being soaked up by backup or clone functions.
Keep in mind that the backup is a real full backup. It doesn’t have a reliance on the source VM, unlike some storage snapshots or vSphere snapshots. Taking a backup of a VM does not alter the way it’s IO is processed and the backup is fully independent and will continue to be fully viable after the source VM is deleted or corrupted.

## Slide 10: Data migration
Data Management Layer
File System
x86 platform
x86 platform
x86 platform
Hypervisor
Hypervisor
Hypervisor
Presentation Layer
VM1
Datastore 1
VM2
Object Store
VM1
VM3
VM4
VM5
VM5
Datastore 2
VM4
VM3
VM2
VM1
VM3
High-level description of process
Move and remote backup are the same operation
Data Management Layer
File System
x86 platform
x86 platform
x86 platform
Hypervisor
Hypervisor
Hypervisor
Presentation Layer
VM1
Datastore 1
VM2
Object Store
VM1
VM3
VM4
VM5
VM5
Datastore 2
VM4
VM3
VM2
VM1
VM3
Data Virtualization Platform
VM4
VM1
VM2
VM5
VM3
VM4
VM1
VM2
VM5
VM3
VM4
Notes: Now that we have seen backups and clones working inside a single SimpliVity Data Center, we need to look at what happens between data centers.
On the left we have our Data Center where we have been taking backups. On the right we have another datacenter in the same Federation.
We set our VM policies at the Federation level, and can have VMs backed up to remote Data Centers in the same Federation. We can also restore VMs to another Data Center and move VMs between datacenters.
At the high level it is very similar: copy the data container and choose whether to update the presentation layer.
<click>
For a backup, the data container at the destination is not presented, if we were moving a VM to the second Data Center, then the presentation layer at the destination would be updated.
The big difference with the remote backup and move operations is that there is no guarantee that we have all of the unique blocks in the object store at the destination. If the data container uses unique blocks that are not at the destination then just those missing unique blocks will need to be copied across the WAN.
<click>
This is where SimpliVity can provide significant benefit in WAN efficiency.

## Slide 11: Data Availability

## Slide 12: OmniStack Storage HA (IP Failover)
The hypervisor accesses OVC by it’s Storage IP address
When an OVC fails its Storage IP is added to another OVC
IP Failover happens fast, no VM IO is lost
The IP returns when the OVC returns
VM
VM
OVC
VM
VM
VM
VM
VM
OVC
VM
VM
VM
VM
VM
OVC
VM
VM
VM
10.40.12.6
10.40.12.7
10.40.12.8
10.40.12.6
Notes: Each hypervisor host accesses its local OmniStack Virtual Controller using a unique storage IP address.
<click>
When one OmniStack Virtual Controller fails its storage IP address is assigned to another OmniStack Virtual Controller. The VMs on the affected node will now use the other OmniStack Virtual Controller for all storage I/O.
This failover needs to be fairly fast, faster than the VM will give up on the I/O. On vSphere this I/O timeout is set to 60 seconds when the VMTools are installed.
<click>
When the failed OmniStack Virtual Controller comes back up it’s IP address transitions back and the hypervisor will access it’s local OmniStack Virtual Controller and everything is back to normal.
IP failover is a crucial part of being resilient to issues in the OmniStack Virtual Controller.

## Slide 13: Protecting Your Data
RAIN vs. RAIN + RAID
Data Protection with RAIN + RAID (SimpliVity)
SSD
SSD
HDD
SSD
EXSi
VM
VM
SVT
VM
HDD
HDD
HDD
HDD
SSD
SSD
HDD
HDD
EXSi
VM
SVT
HDD
HDD
HDD
HDD
SSD
SSD
HDD
HDD
EXSi
VM
VM
SVT
VM
HDD
HDD
HDD
HDD
VM
SSD
SSD
HDD
HDD
EXSi
VM
VM
SVT
VM
HDD
HDD
HDD
SSD
VM
VM
VM
x
x
x
x
x
x
x
x
x
x
x
x
Notes: Let’s now contrast the RAIN-based architecture with how SimpliVity protects data. We didn’t want to be known as just “A VDI Appliance” but wanted to go after the true datacenter space, which are the mission-critical application servers. There are significant differences on how you need to protect your data when you go after the bloodline of your business, the data, vs. your desktops, and SimpliVity recognizes this, which is why we combined two data resiliency technologies into our platform.
SimpliVity came to market with a RAIN + RAID architecture vs. most of our competitors only using RAIN. There are significant differences in these two architectures that we really need to point out. I’m going to start simulating some drive failures here, feel free to interrupt me when you think SimpliVity has lost data.
<start clicking – note that you do not have to count your clicks (13 if you want to), just keep an eye on the slide until you see a little black dot at the top right corner of the slide, once it appears, stop clicking>
All of these failures will not result in any data loss. In fact, all the data is still fully available. At this point, we’ve lost 12 drives across this 4 node cluster and SimpliVity still has 100% data integrity. Pretty good right? But that’s not the end
<click>
If someone goes behind one of these nodes and pulls the plug or something happens to the node itself VMware HA will kick in, restart your virtual machines on the remaining nodes and you’ll STILL have all data available.
So let me ask you this, which one of these would you rather put your servers and data on? Sure, I work for SimpliVity but … it’s pretty clear to me that I would rather have a RAIN + RAID architecture vs. simply RAIN.
<end of slide>
A few notes on this slide:
This example uses the CN-2400 as an example to avoid the additional complexities of having 2 RAID6 sets. You can note that models with more disks could tolerate additional disk failures, assuming only the right disks fail.
4 nodes were used purposefully:
  Nova cannot claim RF3 with this example
  This also includes the VSAN-based models that start with a minimum of 4 nodes
    Note that someone could call you our with VM level RF3 with VSAN. Be prepared that explain that there are “exceptions” to the rule, however, they take up much more space to achieve this.
The yellow “X” on the SSD is not to represent some weird state of the drive, red on red does not show up very well.

## Slide 14: Protecting Your Data
RAIN + RAID vs. RAIN
Data Protection with RAIN
SSD
SSD
HDD
HDD
EXSi
HDD
HDD
HDD
HDD
SSD
SSD
HDD
HDD
EXSi
HDD
HDD
HDD
HDD
SSD
SSD
HDD
HDD
EXSi
HDD
HDD
HDD
HDD
SSD
SSD
HDD
HDD
EXSi
HDD
HDD
HDD
HDD
VM
VM
VM
VM
VM
VM
VM
VM
VM
SVT
SVT
SVT
VM
VM
VM
VM
VM
VM
SVT
x
x
x
Notes: Let’s take a look at the data resiliency across nodes. First, we'll take a look at a generic RAIN (Redundant Array of Independent Nodes) architecture
<click>
1 drive failed
<click>
2 drives failed
<click>
Results in data loss. This is because in a RAIN architecture, your failure domain become the individual disk drives themselves. Let’s take this a step further
<click>
Say you have a node in maintenance mode for whatever reason
<click>
And you have a single drive failure
<click>
Guess what?
<click>
Data availability, possibly data loss.
What’s most likely to fail in your datacenter, something that moves or spins, such as fans, power supplies, or (point to the slide) hard drives; or CPU, motherboard, or RAM? Which most recently failed in your data center?
<end of slide>
A few notes on this slide:
4 nodes were used purposefully:
  Nova cannot claim RF3 with this example
  This also includes the VSAN-based models that start with a minimum of 4 nodes
    Note that someone could call you our with VM level RF3 with VSAN. Be prepared that explain that there are “exceptions” to the rule, however, they take up much more space to achieve this.
The controller virtual machine named as “VSA” as a generic term and doesn’t specifically call anyone out.

## Slide 15: Data Distribution Performance Considerations
No Data Localization
(RF3)
Primary Data Localization (RF2)
Full Data Localization
(RF2)
VM
APP
OS
NODE 1
NODE 2
NODE 3
NODE 4
NODE 5
NODE 6
BEST
PEAK PERFORMANCE
GOOD
GOOD
FAIR
BEST
PREDICTABLE PERFORMANCE
POOR
POOR
FAIR
Full Data Localization provides most Predictable Performance
  Data ALWAYS stored local to the VM, even when VM is moved
  Data never need to be “re-localized”
  Fully exploits speed of all-flash storage.
Full Data Localization provides best Peak Performance.
  Data ALWAYS stored local to the VM
  Lowest overhead in write operations
Primary Data Localization
(RF3)
Notes: Imagine if you will that we've got a six-note cluster here and imagine that in this cluster we have a virtual machine running on note one. Now the first architecture we're going to talk about this is full data localization and with full data localization we have a primary copy of our virtual machine that's running completely localized to one note and we're going to have a secondary copy of that virtual machine that is completely localized to another note. In the SimpliVity world we actually take it a step further to ensure that the virtual machine is always running local to its data. So, we actually have what we call intelligent workload optimizer that make sure that the virtual machine through integration with DRS is always running in this instance on note one or note two.
The second way of dealing with data localization within hyper infrastructure is primary data localization also referred to as primary copy localization. Primary data localization is where we take the primary copy of the virtual machine and we localize that to a single note. The secondary copy of that virtual machine is actually spread out through other notes within the cluster. Now, whether it's RF2 or RF3, RF3 just keeps additional copies of that virtual machines spread out throughout the cluster. As you can see this allows us to keep a local copy and get the benefits of some level of data localization but the secondary copy is spread out. In these kind of architectures it really isn't data localization that the provider's delivering what it is, is its data re-localization. The provider is allowing you that when you move the virtual machine to another note we're going to re-localize the data, but that's going to have some impacts on performance in the predictable nature of performance, you just not going to be able to predict what that impact is going to be and how that's going to be perceived by your applications and users.
The third way of doing data localization is really not to do data localization at all or no data localization, and this is where both the primary copy of the VMs data, as well as the secondary copy is spread throughout the entire cluster. Imagine if you will that we have a failure of note one, after note one fails the virtual machine is going to be restarted on another note using HA. In this instance with full data localization there's no real impact to performance other than possibly reheating the cash. All of the data for this virtual machine is local and we can go straight down to access that virtual machine. There's no need to re-localize the data bring the blocks across the network or figure out where those box actually are in the first place we know that they're all local, but with primary data localization we now have to go and search out these blocks throughout the cluster and figure out where these blocks located and possibly re-localize them now to note two so that we can establish data localization again.
In the no data localization architecture of course there really isn't much difference in the performance from when we were running on note one to when we were running on note two because we consistently have to go across the network to find where these pieces of data are bring them back to this note. Now where this comes into play and why this architecture is important is when we start to talk about predictable performance, full data localization provides the most predictable performance, it always ensures that the data is stored local to the virtual machine even if that VM is moved due to something like an HA event. This ensures that data never needs to be re-localized, it also is going to fully exploit the speed of all flash storage because when we have to go across the network that's going to be significantly more noticeable in an all flash world than perhaps in a hybrid world.
It also is going to fully exploit the speed of all flash storage as we move into the all flash world full data localization is going to enable us to have the best performance on all flash. And when we start to talk about peak performance full data localization is also going to provide the best peak performance especially as we talk about failovers and similar because the data is always stored local to the VM. And when it comes to doing a secondary or an HA write operation we don’t have to figure out and take the time to determine how we want to distribute that secondary write across the cluster. In our world that secondary write is always near to the note two in this example, whereas with primary data localization you have to figure out which note you potentially want to mirror this data to or maybe if you're updating a block you have to figure out where that block was previously located and update that location. You can have a noticeable amount of performance overhead. In no data localization, of course we constantly have to go over the network to receive any kind of data for our virtual machine which has fairly noticeable impacts both the predictable nature of performance as well as the peak performance.

## Slide 16: Failure Scenario

## Slide 17: SimpliVity 2+1 Federation
Primary Datacenter
Secondary Datacenter
This Represents a Typical SimpliVity 2+1 Federation Deployment.
Single Points of Failure are Minimized Using Multiple OmniCubes, Network Connection Redundancy, RAID Protection on Local Disks, and Off Site Replication.
Data is Protected Across Sites Using SimpliVity Backups Which are Replicated Between Datacenters.

## Slide 18: SimpliVity Local VM Recovery
Primary Datacenter
Secondary Datacenter
Virtual Machines Backup Policies are Configured to Create Local Backups of Virtual Machines in the Primary Datacenter.
If a Virtual Machine Fails
or is Deleted.
The Virtual Machine can be Quickly Restored from the Local Backup.
File Level Restore is Available to Quickly Restore Individual Files and/or Folders to a Virtual Machine.

## Slide 19: SimpliVity Component Failure Recovery – Hard Disk
Primary Datacenter
Secondary Datacenter
Two Hard Disk Failures. No Impact on Virtual Machine Availability.
Third Hard Disk Failure. Storage Traffic Fails Over. Virtual Machines Continue to Run.

## Slide 20: SimpliVity Component Failure Recovery – OmniStack Accelerator/OVC
Primary Datacenter
Secondary Datacenter
Storage Traffic Fails Over.
Virtual Machines Continue to Run.
Failure of OmniStack Accelerator Card or OmniCube Virtual Controller (OVC)

## Slide 21: SimpliVity Node Failure Recovery
Node Failure in Primary Datacenter Power Outage Hardware Failure
vSphere HA Triggered
HA Restarts VMs on Surviving Node
Primary Datacenter
Secondary Datacenter

## Slide 22: SimpliVity Remote VM Recovery
Primary Datacenter
Secondary Datacenter
Virtual Machines Backup Policies are Configured to Send Backups to Secondary Datacenter
A Complete Site Failure Requires Virtual Machines to be Restored at Secondary Datacenter
Virtual Machines are Restored from SimpliVity Backups in Secondary Datacenter

## Slide 23: SimpliVity Failback
Primary Datacenter
Secondary Datacenter
The Primary Datacenter is Back Online After an Outage
SimpliVity Move is Then Used to Move Virtual Machines from the Secondary Datacenter back to the Primary Datacenter

## Slide 24: SimpliVity 2+1 Availability Best Practices
vCenter Servers Running in both the Primary Datacenter and Secondary Datacenter Configured in Linked-Mode.
SimpliVity Backup Policies Should be Configured to Schedule Backups of Virtual Machines to Both the Primary Datacenter and the Secondary Datacenter.
OmniCube Power Supplies Should be Connected to Separate PDUs Serviced by Separate UPS Protected Circuits.
Virtual Machine and Management Networks Should be Connected Across Multiple Physical Switches.

## Slide 25: Thank you